//======================================================================
      // ASSIGNMENT : CODE CONVERSION

//=====================================================================
section .data

menumsg db 10,10,'Menu:' ;menu
db 10,'1) Hex to BCD'
db 10,'2) BCD to Hex'
db 10,'3) Exit'
db 10,10,'Please Enter Choice :'
menumsg_len equ $-menumsg ;length of menu

wrchmsg db 10,10,'Invalid choice....Please try again!!!',10,10
wrchmsg_len equ $-wrchmsg ;wrong choice message and its length

hexinmsg db 10,10,'Enter a 4 digit hex number :'
hexinmsg_len equ $-hexinmsg ;message for hex number and its length

bcdopmsg db 10,10,'Its BCD Equivalent :'
bcdopmsg_len equ $-bcdopmsg ;message for BCD number and its length

bcdinmsg db 10,10,'Enter 5 digit BCD number :'
bcdinmsg_len equ $-bcdinmsg ;message for BCD number and its length

hexopmsg db 10,10,'Its Hex Equivalent :'
hexopmsg_len equ $-hexopmsg ;message for hex number and its length
;----------------------------------------------------------------------------------------------- -----------------------
section .bss
numascii resb 06 ;numascii buffer for choice, hex and bcd input
opbuff resb 05 ;reserved 05 bytes for opbuff(hex to BCD)
dnumbuff resb 08 ;reserved 08 bytes for dnumbuff(BCD to hex)
;----------------------------------------------------------------------------------------------- -----------------------
%macro dispmsg 2 ;define macro along with parameters
mov rax,1 ;standard output
mov rdi,1 ;input write
mov rsi,%1 ;display message address
mov rdx,%2 ;message length
syscall ;interrupt for kernel in 64-bit
%endmacro

%macro accept 2 ;define macro along with parameters
mov rax,0 ;standard input
mov rdi,0 ;standard read
mov rsi,%1 ;display message address
mov rdx,%2 ;message length
syscall ;interrupt for kernel in 64-bit
%endmacro
;----------------------------------------------------------------------------------- -----------------------------------
section .text
global _start ;starting of the program
_start:

dispmsg menumsg,menumsg_len ;to display the menu and take its length
accept numascii,2 ;accepting numbers

case1:
cmp byte[numascii],'1' ;compare entered choice with 1
jne case2 ;if not equal then jump to case 2
call hex2bcd_proc ;calling hex2bcd procedure
jmp _start ;after the procedure is executed jump back to start

case2:
cmp byte [numascii],'2' ;compare entered choice with 2
jne case3 ;if not equal then jump to case 3
call bcd2hex_proc ;calling bcd2hex procedure
jmp _start ;after the procedure is executed jump back to start

case3:
cmp byte [numascii],'3' ;compare entered choice with 3
je exit ;jump if equal to exit
dispmsg wrchmsg,wrchmsg_len ;to display wrong message and take its length
jmp _start ;after displaying wrong message jump to star

exit:
mov rax,01 ;system call for exit
syscall ;interrupt for kernel in 64-bit
;------------------------------------------------------------------------------------- ---------------------------------
hex2bcd_proc:

dispmsg hexinmsg,hexinmsg_len ;to display hex mesaage
accept numascii,5 ;accept 5 numbers
call packnum ;calling packnum procedure
mov rcx,0 ;clear rcx register
mov ax,bx ;move contents of bx register into ax register
mov bx,10 ;move 0Ah into bx register

;-----------------------------------------------------------------------------------------------------------------------
h2bup1:

mov dx,0 ;clear dx register
div bx ;divide ax register by bx register
push rdx ;push the contents of rdx register
inc rcx ;increment the contents of rcx register
cmp ax,0 ;compare ax register contents with 0
jne h2bup1 ;if not equal jump to start of h2bup1 loop
mov rdi,opbuff ;move contents o opbuff buffer to rdi

;-----------------------------------------------------------------------------------------------------------------------
h2bup2:
 pop rdx ;pop the contents of rdx register
add dl,30h ;add 30h to the contents of dl register
mov [rdi],dl ;move contents of dl register into rdi
inc rdi ;increment the contents of rdi
loop h2bup2 ;carry out h2bup loop till the number of counts given

;-----------------------------------------------------------------------------------------------------------------------

dispmsg bcdopmsg,bcdopmsg_len ;display the bcd numbers obtained message
dispmsg opbuff,5 ;to diplay the result of conversion
ret ;return

;-----------------------------------------------------------------------------------------------------------------------

bcd2hex_proc:

dispmsg bcdinmsg,bcdinmsg_len ;to display the bcd message
accept numascii,6 ;to accept 6 numbers
dispmsg hexopmsg,hexopmsg_len ;display the hex message
mov rsi,numascii ;move contents of numascii buffer into rsi
mov rcx,05 ;store the count 5 in rcx register
mov rax,0 ;clear the rax register
mov rbx,0ah ;move oah(10) into the rbx register

;-----------------------------------------------------------------------------------------------------------------------
b2hup1:

mov rdx,0 ;clear the rdx register
mul rbx ;multiply rax register with rbx register
mov dl,[rsi] ;move contents of rsi into dl register
sub dl,30h ;subtract 30h from the contents of the dl register
add rax,rdx ;add contents of rdx into rax
inc rsi ;increment contents of rsi
loop b2hup1 ;carry out loop b2hup1 till the number of counts given
mov rbx,rax ;move contents of rax register into rbx register
call disp32_num ;calling the disp32_num procedure
ret ;return

;-----------------------------------------------------------------------------------------------------------------------
packnum:

mov bx,0 ;clear bx register
mov rcx,04 ;count of 4 for enter 4 hex numbers

mov rsi,numascii ;move contents of numascii into rsi
        ;takes ascii value of entered number
;-----------------------------------------------------------------------------------------------------------------------
up1:

rol bx,04 ;rotate the value in bx register by 4 counts
mov al,[rsi] ;move contents of rsi(ascii value) into al registers
cmp al,39h ;compare contents of al register with 39h
jbe skip1 ;if compared value is below(less) than 39h then jump to skip1

sub al,07h ;if compared value is greater than 39h
        ;then subtract 07h from contents of al register
;-----------------------------------------------------------------------------------------------------------------------
skip1:

sub al,30h ;subtract 30h from the contents of al register
add bl,al ;add the contents of al register to the bl register
inc rsi ;increment the contents of rsi
loop up1 ;perform the loop up 1 functions again
ret ;return

;-----------------------------------------------------------------------------------------------------------------------
disp32_num:

mov rdi,dnumbuff ;move contents of dnumbuff buffer to rdi
mov rcx,08 ;move 08 into the rcx register

;-----------------------------------------------------------------------------------------------------------------------
dispup1:

rol ebx,4 ;rotate the contents of ebx register by 4 counts
mov dl,bl ;move contents of bl register into dl register
and dl,0fh ;and ofh with contents of dl register
add dl,30h ;add 30h to the contents of dl register
cmp dl,39h ;compare contents of dl register with39h
jbe dispskip1 ;if compared value is below(less) than 39h then jump to dispskip1
add dl,07h ;add 07h to the contents of dl register

;-----------------------------------------------------------------------------------------------------------------------
dispskip1:

mov [rdi],dl ;move contents of dl register into rdi
inc rdi ;increment rdi
loop dispup1 ;carry out the loop dispup1 again
dispmsg dnumbuff+3,5 ;display message
ret ;return

;-----------------------------------------------------------------------------------------------------------------------
.................................................................OUTPUT.............................................................................
admin1@admin:~$ nasm -f elf64 BCD.asm
admin1@admin:~$ ld -o BCD BCD.o
admin1@admin:~$ ./BCD
Menu:
1) Hex to BCD
2) BCD to Hex
3) Exit

Please Enter Choice :1
Enter a 4 digit hex number :ABDF
Its BCD Equivalent :43999

Menu:
1) Hex to BCD
2) BCD to Hex
3) Exit

Please Enter Choice :2
Enter 5 digit BCD number :2468
Its Hex Equivalent :06142

Menu:
1) Hex to BCD
2) BCD to Hex
3) Exit
Please Enter Choice :3
admin1@admin:~$