        // ASSIGNMENT : MULTIPLICATION

        %macro dispmsg 2 ;macro for display
   mov rax,1 ;standard ouput
   mov rdi,1 ;system for write
   mov rsi,%1 ;display message address
   mov rdx,%2 ;display message length
   syscall ;interrupt for 64-bit
%endmacro ;close macro

%macro exitprog 0 ;macro for exit
mov rax,60 ;system for exit
mov rdx,0
syscall ;interrupt for 64-bit
%endmacro ;close macro

%macro gtch 1 ;macro for accept
   mov rax,0 ;standard input
   mov rdi,0 ;system for read
   mov rsi,%1 ;input the message
   mov rdx,1 ;message length
   syscall ;interrupt for 64-bit
%endmacro ;close macro
;--------------------------------------------------------------------------------------------------------------------------------------
section .data
nwline db 10
m0 db 10,10,"Program to multiply two numbers using successive addition and add-and-shift method"
l0 equ $-m0
m1 db 10,"1. Successive Addition method",10,"2. Add-and-Shift method",10,"3. Exit",10,10, "Enter your choice (1/2/3 <ENTER>): "
l1 equ $-m1
m2 db 10,"Enter multiplicand (2 digit HEX no) : "
l2 equ $-m2
m3 db 10,"Enter multiplier (2 digit HEX no) : "
l3 equ $-m3
m4 db 10,"The Multiplication is : "
l4 equ $-m4
;----------------------------------------------------------------------------------------------------------------------------------------
section .bss
mcand resq 1 ;reserve 1 quad for multiplicand
mplier resq 1 ;reserve 1 quad for multiplier
input resb 1 ;reserve 1 byte for input
output resb 1 ;reserve 1 byte for output
choice resb 1 ;reserve 1 byte for choice
;-----------------------------------------------------------------------------------------------------------------------------------------
section .text
global _start ;starting of main program
_start :

dispmsg m0,l0 ;Displaying the menu

back:
dispmsg m1,l1	;Displaying the first message
gtch input ;To read and discard ENTER key pressed.

mov al, byte[input]	;Get choice
mov byte[choice],al

gtch input	;To read and discard ENTER key pressed.

mov al, byte[choice]

cmp al, '1' ;compare contents of al with 1
je succ_add ;if equal the jump to succ_add procedure

cmp al, '2' ;compare the contents of al with 2
je shft_add ;if equal the jump to shft_add procedure

cmp al, '3' ;compare the contents of al with 3
jnz back ;if not zero then jump to back
exitprog ;exit program
;-----------------------------------------------------------------------------------------------------------------------------------------
; SUCCESSIVE ADDITION
        succ_add: ;succ_add procedure
dispmsg m2,l2 ;Displaying the second message
call getnum ;call getnum procedure
mov [mcand],rax ;mov contents of rax(multiplicand) into mcand buffer
gtch input ;To read and discard ENTER key pressed.

dispmsg m3,l3 ;Displaying the third message
call getnum ;call getnum procedure
mov [mplier],rax ;mov contents of rax(multiplier) into mplier buffer
gtch input ;To read and discard ENTER key pressed.mov rax,0
dispmsg m4,l4 ;Displaying the fourth message

mov rax,0 ;clearing rax register
cmp qword[mplier],0 ;compare contents of mplier buffer in qword with 0
jz ll5 ;if zero jump to loop 5
;----------------------------------------------------------------------------------------------------------------------------------------
ll1: ;loop 1
add rax,qword[mcand] ;add contents of mcand buffer in qword to contents of rax register
dec qword[mplier] ;decrement contents of mplier buffer
jnz ll1 ;if not zero jump to loop 1
;----------------------------------------------------------------------------------------------------------------------------------
ll5: ;loop 5
call disphx16	;call disphx16 procedure to displays a 8 digit hex number in rax
jmp back ;jump to back after execution
;----------------------------------------------------------------------------------------------------------------------------------
; ADD & SHIFT
shft_add: ;shft_add procedure
dispmsg m2,l2	;Displaying the second message
call getnum ;call getnum procedure
mov [mcand],rax	;mov contents of rax(multiplicand) into mcand buffer
gtch input	;To read and discard ENTER key pressed.

dispmsg m3,l3	;Displaying the third message
call getnum ;call getnum procedure
mov [mplier],rax ;mov contents of rax(multiplier) into mplier buffer
gtch input	;To read and discard ENTER key pressed.

mov rax,0 ;clearing the rax register
dispmsg m4,l4 ;Displaying the fourth message

mov rax,0 ;clearing the rax register
mov rcx,8 ;taking count of 8 in rcx register
mov rdx,qword[mplier]	;multiplier is 8 bits so it occupies dl
mov rbx,qword[mcand]	;mupltiplicand is 8 bits so it occupies bl

        ;we will put Q in higher 8 bits of ax (i.e. ah)
        ;and multipler in lower 8 bits of ax (i.e. al)

        mov ah,0 ;clearing ah register
mov al,dl ;ah already 0 and al now contains multiplier
;------------------------------------------------------------------------------------------------------------------------------------------
ll3: ;loop 3 (s3)
mov dh,al ;mov contents of al into dh as dh is used as temporary
and dh,1 ;check d0 bit of multiplier
jz ll8 ;if d0 bit was zero, Z flag will be set (s2)(if zero jmp to loop 8)
add ah, bl ;d0 bit of multiplier is set
        ;so add multiplicand to Q(add bl into ah)
;-------------------------------------------------------------------------------------------------------------------------------------------
ll8: ;loop 8 (s2)
shr ax,1 ;shift both Q (ah) and muplitiplier (al) right 1 bit
dec rcx ;decrement contents of rcx
jnz ll3 ;if not zero then jump to loop 3 (s3)
call disphx16 ;call procedure disphx16
jmp back ;jump to back
;------------------------------------------------------------------------------------------------------------------------------------------
getnum: ;Procedure to get a 2 digit hex no from user
        ; number returned in rax
mov cx,0204h ;02 digits to display and 04 count to rotate
mov rbx,0 ;clearing rbx register
;-------------------------------------------------------------------------------------------------------------------------------------------
ll2: ;loop 2
push rcx	;syscall destroys rcx.Rest all regs are preserved
gtch input ;To read and discard ENTER key pressed.
pop rcx ;pop the contents of rcx

        mov rax,0 ;clearing the contents of rax
mov al,byte[input] ;Get choice
sub rax,30h ;subtract 30h from contents of rax
cmp rax,09h ;compare the contents of rax register with 09h
jbe skip1 ;if equal then jump below to skip1 label
sub rax,7 ;subtract 7 from contents of rax register
;------------------------------------------------------------------------------------------------------------------------------------
        skip1: ;skip1 label
shl rbx,cl ;shift multiplicand and count to the left
add rbx,rax ;add contents of rax register to the contents of rbx register
dec ch ;decrement the contents of ch register
jnz ll2 ;if not zero then jump to loop 2
mov rax,rbx ;mov contents of rbx register into rax register
ret ;return
;---------------------------------------------------------------------------------------------------------------------------------------
disphx16: ;Displays a 16 digit hex number passed in rax
mov rbx,rax ;move contents of rax register into rbx register
mov cx,1004h	;16 digits to display and 04 count to rotate
;---------------------------------------------------------------------------------------------------------------------------------------
ll6: ;loop 6
rol rbx,cl ;rotate multiplicand and count to the left
mov rdx,rbx ;mov contents of rbx register into rdx register
and rdx,0fh ;anding contents of rdx register with 0fh
add rdx,30h ;adding contents of rdx register with 30h
cmp rdx,039h ;comparing the contents of rdx register with 39h
jbe skip4 ;if equal then jump below to skip4 label
add rdx,7 ;add 7 to the contents of rdx register
;-----------------------------------------------------------------------------------------------------------------------------------------
skip4: ;skip4 label
mov byte[output],dl ;mov contents of dl register into output buffer in bytes
push rcx ;push the contents of rcx register
dispmsg output,1 ;Displaying the output
pop rcx ;pop the contents of rcx
dec ch ;decrement the count(contents of ch)
jnz ll6 ;if not zero the jump to loop 6
ret ;return
.................................................OUTPUT....................................................
admin1@admin:~$ nasm -f elf64 multi1.asm
admin1@admin:~$ ld -o multi1 multi1.o
admin1@admin:~$ ./multi1
Program to multiply two numbers using successive addition and add-and-shift method
1. Successive Addition method
2. Add-and-Shift method
3. Exit
Enter your choice (1/2/3 <ENTER>): 1
Enter multiplicand (2 digit HEX no) : 02
Enter multiplier (2 digit HEX no) : 06

The Multiplication is : 000000000000000C
1. Successive Addition method
2. Add-and-Shift method
3. Exit

Enter your choice (1/2/3 <ENTER>): 2
Enter multiplicand (2 digit HEX no) : 03
Enter multiplier (2 digit HEX no) : 05
The Multiplication is : 000000000000000F
1. Successive Addition method
2. Add-and-Shift method
3. Exit
Enter your choice (1/2/3 <ENTER>): 3
admin1@admin:~$